## Slide 1: Juelich Summer School in Fire Dynamics Modeling (Turbulent) Combustion
Randy McDermott

## Slide 2
COMBUSTION (0.5 DAYS) | PREVIOUS KNOWLEDGE | COURSE LEARNING OUTCOMES |  | 
 | KNOWS BEFORE Refers to previous knowledge that is assumed. | MUST KNOW Refers to knowledge and skills that are absolutely necessary. | SHOULD KNOW Should know includes the details and extensions to core content theories, models and principles. | NICE TO KNOW Nice to know supplements the core content and should know with details.
Scientific competence; what does the student know about theory. | Basic chemistry and thermodynamics, including: Stoichiometry Ideal gas equation of state First Law of Thermodynamics Internal energy, sensible and chemical enthalpy Mathematical background in simple ODEs and basic linear algebra | Can explain how the fuel properties affect the fire’s heat release rate Can write chemical reactions in terms of lumped species Can explain how turbulence affects the heat release rate (EDC model) Can describe the various modes of flame suppression | Can define the chemical heat release rate per unit volume Understands the concept of mixture fraction and its relationship to local species composition and flame temperature Can describe how the mixing time scale changes with grid resolution Can explain the concept of the critical flame temperature | Understands the difference between scalar mixing and turbulent transport. Understands the concept of a subgrid PDF. Can discuss the relationship between Damköhler number and flame extinction
Professional competence and skills; what the student knows and can do in practice. | Can run FDS-simulations Can use Matlab or Python to analyze FDS output | Can specify FDS inputs for combustion model Can modify the FDS verification tests | Can discuss various methods of generating CO and soot in FDS | Can solve a system of ODEs for finite-rate kinetics using FDS

## Slide 3: Outline
Thermochemistry
  stoichiometry
  realizability
  thermodynamics
  infinitely fast / equilibrium / finite-rate chemistry
  mixture fraction / lumped species
  specified product yields
  complex fuel mixtures
Eddy Dissipation Concept
  subgrid distributions in species and temperature
  rate of turbulent mixing
  mixing vs. transport
Flame Extinction
  critical flame temperature / ignition temperature
  droplet evaporation
  strained laminar flames (flamelets)
  Damköhler number

## Slide 4: Recommended Reading
H. Scott Fogler, “Elements of Chemical Reaction Engineering”, Prentice-Hall, 1992.
Stephen R. Turns, “An Introduction to Combustion”, McGraw-Hill, 2000.
Norbert Peters, “Turbulent Combustion”, Cambridge, 2000.
Rodney O. Fox, “Computational Models for Turbulent Reacting Flows”, Cambridege, 2003.
Thierry Poinsot and Denis Veynante, “Theoretical and Numerical Combustion”, Edwards, 2005.

## Slide 5: Module I: Thermochemistry

## Slide 6: Stoichiometry
COMPLETE COMBUSTION
Propane, C3H8
http://commons.wikimedia.org/

## Slide 7: Complex Fuels
https://upload.wikimedia.org/wikipedia/commons/thumb/a/a4/Cellulose_strand.svg/1131px-Cellulose_strand.svg.png
http://www.todayifoundout.com/index.php/2013/08/why-doesnt-wood-melt/
Cellulose
D. Drysdale, Table 5.14
CH2O

## Slide 8: Complex Chemistry
A. Dmitriev et al. DOI: 10.1016/j.combustflame.2015.07.032
S. Shuai, Z. Wang, H. Xu. Internal Combustion Engine Simulation, 2015.
TEM image of a typical aircraft combustor soot aggregate. (a) aggregate and (b) detail of the surface. Adapted from Popovitcheva et al. (2000)
https://faculty.kaust.edu.sa/sites/fabriziobisetti/Pages/particulates.aspx
GRI-Mech 3.0
53 species
400+ reactions

## Slide 9: Ideal Gas Equation of State
mass density [kg/m^3]
background pressure [Pa]
mixture molecular weight [kg-mixture/kmol-mixture]
universal gas constant [8314.5 Pa.m^3/(kmol.K)]
temperature [K]

## Slide 10: Mixture Molecular Weight

## Slide 11: Mixture Molecular Weight (Mass Fractions)

## Slide 12: Mixture Molecular Weight (Mass Fractions)

## Slide 13: Realizable Species Mass Fractions
Realizability requires
Dan Swenson
Thunderhead Engineering
2015 Boris Stock Award
Guaranteed to be realizable
(See realizable_mass_fractions.fds)

## Slide 14: Heat of Combustion
heat of formation [J/kg-alpha]
stoichiometric coefficient for
species alpha in reaction i
reactants negative
products positive
stoichiometric coefficients represent moles of alpha
produced per mole of fuel reacted
for reaction i

## Slide 15: Heat of Combustion - Oxygen Basis
EPUMO2
HEAT_OF_COMBUSTION

## Slide 16: Example: Heat of Combustion for Propane
Species | Molecular Weight (kg/kmol) | Enthalpy of Formation (J/kg)
Propane, C3H8 | 44.09562 | -2.37E+06
Oxygen, O2 | 31.99880 | 0
Carbon Dioxide, CO2 | 44.00950 | -8.94E+06
Water Vapor, H2O | 18.01528 | -1.34E+07
Run HOC.py
approx 13,000 kJ/kg O2

## Slide 17: Equivalence Ratio
Generally, fuel rich conditions
are responsible for producing CO
and soot.

## Slide 18: Adiabatic Flame Temperature
change in
internal energy
heat transferred
to the system
work done
on the system
First Law of
Thermodynamics
Recall the definition of
enthalpy:

## Slide 19: Adiabatic Flame Temperature Example: Stoichiometric Propane in Dry Air
T_0 = 20 C
HOC = 2.04e6 kJ/kmol C3H8 reacted
C_p = 37 kJ/kmol/K

## Slide 20: Mixture Fraction (Non-premixed Flames)
Fuel, f=1
Air, f=0
Air, f=0

## Slide 21: Mixture Fraction (Non-premixed Flames)
Fuel, f=1
Air, f=0
Air, f=0

## Slide 22: Mixture Fraction is a Conserved Scalar
The mixture fraction is neither created nor destroyed locally, only transported.
Assuming all species have equal diffusivities, D [m^2/s], the mixture fraction evolves by
No source term!
Question: Is mixture fraction a passive scalar?

## Slide 23: Infinitely Fast Chemistry
Imagine that the rate of chemical kinetics is much much faster than the rate of mixing. In such a scenario, (for now ignoring the possibility of extinction) fuel and air cannot coexist because all of the limiting reactant is immediately converted to products.
The local value of mixture fraction directly determines the local composition (mass fractions of Fuel, Air, and Products).

## Slide 24: Burke-Schumann Solution - Stoichiometric
@
Question: How do you determine s?

## Slide 25: Burke-Schumann Solution - Fuel Rich
@

## Slide 26: Burke-Schumann Solution - Fuel Lean
@

## Slide 27: Burke-Schumann Solution - Temperature

## Slide 28: Burke-Schumann Solution
(See burke-schumann.py)

## Slide 29: Equilibrium Chemistry
https://chem.libretexts.org
NASA CEA code

## Slide 30: Finite-Rate Chemistry
Arrhenius rate constant
[appropriate units]
pre-exponential factor
[appropriate units]
activation energy [J/(mol K)]

## Slide 31: Finite Rate Chemistry - Mass Fractions
primitive species

## Slide 32: Example: Westbrook and Dryer
Run reactionrate_arrhenius_2order_1step.fds
Plot the time history of species mass fractions
Modify the realizable_mass_fractions.fds case to use the Westbrook and Dryer propane reaction parameters (see FDS User Guide example).
Plot the global combustion efficiency as a function of time.

## Slide 33: Rate Laws
Stoichiometry:
Mixture fraction (still):
reaction
model
But now need to solve 2
transport equations, because
Fuel and Air can coexist.

## Slide 34: Reaction Progress Variables
In general, the system can be defined in terms of the mixture fraction and a reaction progress variable.
In FDS, we choose to use lumped species mass fractions as progress variables.
This avoids complications related to defining boundary conditions for the generalized progress variable approach.

## Slide 35: Lumped Species
Let’s go back to our propane reaction and write it two equivalent ways:
Air
Products
Fuel
Question: How do you determine NA , NP?

## Slide 36: Lumped Species
Lumped species are groups of primitive species that transport and react together, implying equal diffusivities for the primitive species within the group.
 | Lumped Species |  | 
Primitive Species | Fuel | Air | Products
C3H8 | 1 | 0 | 0
O2 | 0 | X_O2,A | 0
N2 | 0 | X_N2,A | X_N2,P
CO2 | 0 | 0 | X_CO2,P
H2O | 0 | 0 | X_H2O,P
SUM | 1 | 1 | 1

## Slide 37: Lumped Species
Question: What is NA WA/WF ?

## Slide 38: Lumped Species Mass Fractions
Recall:
Fuel
Air
Products
elements of A:

## Slide 39: Example: Lumped Species to Primitive Species
(See Z2Y.py)

## Slide 40: Specified CO and Soot Yields
C0.9H0.1
Ws=10.9 kg/kmol
SOOT_YIELD

## Slide 41: Complete “Simple” Hydrocarbon Chemistry

## Slide 42: Example: Simple Chemistry with FORMULA
Run simple_chemistry_methane.fds
Modify input file for CH2O using FORMULA
Add specified HEAT_OF_COMBUSTION
Add a CO_YIELD and a SOOT_YIELD
Examine the .out file for each case.

## Slide 43: Heat Release Rate
FDS computes HRR both ways, but first method
is what gets used in energy equation.
Example: hrrpuv_reac_simple.fds
plot hrrpuv
plot hrrpuv reac

## Slide 44: Example: Custom Fuel Mixture
Create a test case with the following natural gas fuel composition.
Replace NITROGEN with CHLORINE. What happens?

## Slide 45: Example: Complex Stoichiometry
Define primitive species in FDS input file.
Define AIR and PRODUCT species.
Determine PRODUCT volume fractions and reaction coefficients.
Add slice output for HCl.
(See fds_complex_stoichiometry.py)

## Slide 46: Module II: Eddy Dissipation Concept (EDC)

## Slide 47: Filtered Species Transport Equation
In LES, the filtered chemical source term
is unclosed.
Filtered field:

## Slide 48: Turbulent Batch Reactor Model

## Slide 49: Turbulence-Chemistry Closure Problem
In general, for finite-rate chemistry the Arrhenius rate laws cannot be evaluated using Favre-filtered fields.
However, the mean may be computed from convolution over the subgrid PDF:
thermochemical composition vector

## Slide 50: Probability Density Functions
Normal distribution:
(See normal_pdf.py)

## Slide 51: Beta PDF
(See beta_pdf.py)
“beta function”

## Slide 52: Example: Dirac Delta Function
Using normal_pdf.py, decrease the variance and plot the results. What do you observe?
The Dirac delta function is defined as
Given your observations from part (a) ,
what is ?
Paul Dirac (1902-1984)

## Slide 53: Multiple Delta Functions
What is the constraint on the weights?

## Slide 54: Lots of Deltas (Particles)

## Slide 55: Lots of Deltas (Particles)

## Slide 56: The First Moment (Mean)
Note: sifting property of Dirac delta function

## Slide 57: The Second (Central) Moment (Variance)

## Slide 58: Example: Computing the Variance

## Slide 59: Example: Computing the Variance

## Slide 60: Interaction by Exchange with the Mean (IEM)

## Slide 61: Example: Evolution of the Variance with IEM
Using the result from the previous slide, derive the evolution equation for the variance according the IEM mixing model.

## Slide 62: Three Environment Subgrid PDF

## Slide 63: Three Environment Subgrid PDF

## Slide 64: Introducing the Unmixed Fraction
true
idealized
“Unmixed Fraction”
Notes: OK, so what we talking about here is closing the mean chemical source term in the LES species transport equation.
In our algorithm, transport is done first, then integration of the reactor model is time split. In this way, each computational cell is treated as a “batch reactor”.
Now, we all understand the the concentration within the cell is not homogenous. In reality, it looks something like the picture on the left. The concept of the TBR model is to decompose the cell into 2 zones, one completely mixed and one completely unmixed, as depicted on the right.
The decomposition is parameterized by a scalar value we call the unmixed fraction. There are two reasons why I chose “unmixed fraction”. The first is that mixed fraction is too close to mixture fraction and these two things are very different. The second reason we’ll see on the next slide.
We have now two compositions, one unmixed and one mixed. Only the mixed composition changes in time during the reactor integration, due to chemical kinetics. What folks seem to have a hard time buying into is that these compositions are, in the concept of this model, the same at the beginning of the reactor substep. If they were not, we would have to transport one of them, and we are trying to avoid that.
I’ll discuss this more in a bit.

## Slide 65: Cell Integral Constraints

## Slide 66: Exercise: Check Cell Integral Constraints

## Slide 67: Unmixed Fraction FAQ
Is the unmixed fraction the same as the mixture fraction?
Is the unmixed fraction related to the mixture fraction?
Why not work in terms of the “mixed fraction”?
Is the unmixed fraction related to the subgrid variance?

## Slide 68: Exercise: Derive Formula for Subgrid Variance Based on Unmixed Fraction (No Reaction)

## Slide 69: Relating Unmixed Fraction and SGS Variance
Notes: So, here is a different look at the subgrid distribution. For now, let’s not consider chemical reaction, so the mixed composition equals the cell mean. Let phi represent a scalar like mass fraction that ranges from 0 to 1.
The plot on the left is another way to look at the subgrid pdf. This cell is completely unmixed (zeta=1) with a cell mean of .5. What is the sgs variance?
Notice that presuming the shape of the pdf allows us to compute the sgs variance from resolved quantities. The variance in this case, which is a maximum, is 0.25.

## Slide 70: Relating Unmixed Fraction and SGS Variance
Notes: OK, let’s do the same exercise for another case. Again, completely unmixed (zeta=1) but now with a mean of .25. The variance drops to about 0.19.

## Slide 71: Relating Unmixed Fraction and SGS Variance
Notes: OK, now let’s consider a slightly more complicated case. Suppose half the cell is mixed and the cell mean is 0.5. Again, the subgrid pdf is displayed on the left, and the variance is, as you can see, lower, for the same cell mean.

## Slide 72: Relating Unmixed Fraction and SGS Variance
Notes: Now let’s again shift the mean to a lower value. You can see that the variance is correspondingly lower.

## Slide 73: Relating Unmixed Fraction and SGS Variance
Notes: OK, so I went though that exercise to get to this plot. What it shows is that you can release sgs variance, zeta, and the cell mean.
It also points out that there is ambiguity in zeta for cells which are pure, which makes sense. However, this introduces complications when it comes to transport.
One of the reasons I want to understand the relationship between zeta and sgs var is that the transport equation for the sgs var is well-understood.

## Slide 74: Evolution of the Unmixed Fraction
Notes: -OK. So one of the key differences between our formulation and others’ is that we are treating the cell like a “batch reactor” (that is, transient) instead of a perfectly stirred reactor (steady state). That is, our unmixed fraction evolves in time. How? (By the way, I can’t really say, at the moment, whether I think this distinction really matters.)
-During the reaction substep (not considering cell to cell transport) the unmixed fraction evolves by this simple ODE. I’ll show why in a minute. Of course, this has a very simple exponential decay solution.
-The plot here shows the initial unmixed fraction starting at 1. This would be the case if all species in the computational cell are initially completely unmixed. So, now you can see why we use the unmixed fraction… so that we have a very simple decay from 1 to 0. But the formulation does not force this as a condition. Zeta_0 can be any value between 0 and 1 and should be related to the cell’s initial scalar variance. This is a part of the model we are still working on. For the moment, we initialize zeta to be 0 in DNS and 1 in LES.
-Now, here is where things get interesting.
-We are now going to derive our chemical source term closure in two different ways.
-First, differential the mean in time.
-Second, plug the PDF into the Fokker-Planck equation and use Interaction by Exchange with the Mixed Mean as the mixing model. Note that this is a slight variant on traditional IEM.
-All roads lead to Rome.
-The key point to take from this slide is that IEMM is our mixing model. And that tau_mix is the mixing time scale you would plug into IEM.

## Slide 75: Fokker-Planck Equation
Derivation 1: Differentiate the mean mass fraction
Derivation 2: Transport of the subgrid PDF (Fokker-Planck)
Notes: -OK. So one of the key differences between our formulation and others’ is that we are treating the cell like a “batch reactor” (that is, transient) instead of a perfectly stirred reactor (steady state). That is, our unmixed fraction evolves in time. How? (By the way, I can’t really say, at the moment, whether I think this distinction really matters.)
-During the reaction substep (not considering cell to cell transport) the unmixed fraction evolves by this simple ODE. I’ll show why in a minute. Of course, this has a very simple exponential decay solution.
-The plot here shows the initial unmixed fraction starting at 1. This would be the case if all species in the computational cell are initially completely unmixed. So, now you can see why we use the unmixed fraction… so that we have a very simple decay from 1 to 0. But the formulation does not force this as a condition. Zeta_0 can be any value between 0 and 1 and should be related to the cell’s initial scalar variance. This is a part of the model we are still working on. For the moment, we initialize zeta to be 0 in DNS and 1 in LES.
-Now, here is where things get interesting.
-We are now going to derive our chemical source term closure in two different ways.
-First, differential the mean in time.
-Second, plug the PDF into the Fokker-Planck equation and use Interaction by Exchange with the Mixed Mean as the mixing model. Note that this is a slight variant on traditional IEM.
-All roads lead to Rome.
-The key point to take from this slide is that IEMM is our mixing model. And that tau_mix is the mixing time scale you would plug into IEM.

## Slide 76: Turbulent Batch Reactor Model

## Slide 77: Limiting Cases: Initially Completely Mixed, Infinitely Fast Kinetics

## Slide 78: Limiting Cases: Initially Completely Unmixed, Infinitely Fast Kinetics

## Slide 79: Basic Eddy Dissipation Concept (Eddy Dissipation Model - EDM)

## Slide 80: Example: Heskestad Flame Height
Run Qs=1_RI=05.fds and visualize HRRPUV in Smokeview
  (modify T_END to 10 s).
Modify the input file to use ZETA_0 = 0 and rerun the case.
Plot HRRPUL vs. Z for both cases.

## Slide 81: Mixing Time Scale

## Slide 82: Exercise: Kolmogorov Scaling
Use a model inertial range energy spectrum to derive the scaling law.
The inertial range spectrum is
grid Nyquist limit
Kolmogorov
constant =
1.5
KE dissipation rate
wavenumber
Andrey Nikolaevich Kolmogorov
(1903 - 1987)

## Slide 83: Module III: Flame Extinction

## Slide 84: Fire Suppression vs. Flame Extinction
Fire suppression mechanisms
  Fuel removal
  Fuel surface cooling
  Remove flame heat feedback
Flame extinction mechanisms
  Thermal extinction
  Aerodynamic quenching
  Kinetic chain breaking

## Slide 85: Binary Flame Extinction for EDC (current state of the art)

## Slide 86: Continuous Flame Extinction for EDC (has been proposed, but under development)
Depending on regime, there could be flame islands within a cell.

## Slide 87: Mechanisms of Flame Extinction
Thermal (FDS)
  Simple (O2 limit, Mowrer)
  Detailed thermophysical properties (Vaari et al.)
Aerodynamic
Kinetic

## Slide 88: O2 Criterion (Mowrer’s Model)
Does not account for Fuel’s heat of combustion
Does not account for the difference between reactant and product thermal properties
Otherwise virtually identical to FDS thermal extinction model (discussed next)
May be used with arbitrarily complex chemistry

## Slide 89: O2 Criterion (Mowrer’s Model)

## Slide 90: Example: Simple Extinction Model
Change the extinction model in Qs=1_RI=05.fds to EXTINCTION 1.
Add a slice file of O2 mass fraction.
Add a slice file of EXTINCTION.

## Slide 91: FDS Thermal Extinction Model
Mass:
Energy:

## Slide 92: FDS Thermal Extinction Model
Diluents include excess FUEL, but not excess AIR.

## Slide 93: FDS Thermal Extinction Model
Diluents include excess FUEL, but not excess AIR.

## Slide 94: Example: FDS Thermal Extinction
Compare flame heights for Qs=1_RI=05.fds with and without SUPPRESSION=F.
Compare flame heights for Qs=1_RI=05.fds with CRITICAL_FLAME_TEMPERATURE=1700 K and 1800 K.

## Slide 95: Simple Ignition Model (AIT)
J.P. White, S. Vilfayeau, A.W. Marshall, A. Trouvé, R.J. McDermott. Modeling flame extinction and reignition in large eddy simulations with fast chemistry. Fire Safety Journal, 2017.
If T_0 > AIT:
  GOTO 2
  ELSE
  Q = 0
CALL EXT MODEL
“AUTO IGNITION TEMPERATURE”

## Slide 96: Example: Cup Burner
Modify the Cup_CH4_N2.fds case
  Change to a single grid
  Reduce resolution by half
  Reduce T_END to 10 s
Replace the “ignitor” with a pilot region above the burner.
  Add an INIT line with AIT=-273 C in same region as ignitor
  Add a SLCF of AIT
  Increase the size of the INIT region

## Slide 97: Aerodynamic Quenching
burning
Da > 1
extinct
Da < 1
CFT is a function of strain
The function is nonlinear
Experimental CFT represents finite strain
Da = 1
Fuel
Oxidizer
x
r
strain rate (1/s)
CFT (K)

## Slide 98: Steady Laminar Flamelet
Fuel
Oxidizer
x
r
Opposed jet diffusion flame
OPPDIFF
Steady, 1D species equation:
Steady, 1D mixture fraction:
Coordinate transformation:

## Slide 99: Steady Laminar Flamelet
Fuel
Oxidizer
x
r
0
from potential flow theory
strain rate

## Slide 100: Damköhler number

## Slide 101: Extension to Premixed Combustion
Treat Mixed Zone as a
Perfectly-Stirred Reactor
from kinetics
Treat Mixed Zone using a
Flame Speed Model
Unburnt
Burnt
Being explored by UTRC
Notes: Well… thus concludes the review. On to premixed combustion.
So, for the batch reactor model, “premixed” simply means zeta_0 < 1. Completely premixed means zeta_0=0. Again, our goal is to accurately integrate the model ODE. This couples the state of mixing with the kinetics.
In moving forward there are basically two approaches: (1) treat the mixed zone as well-stirred or (2) treat the mixed zone with a flame front. Likely, which you choose should depend on the Karlavitz number. But for now I will simply show how to proceed with each approach.
The well-stirred reactor approach is pretty straight forward. Vaidya is using this in his code at UTRC, and they are working with moderately-sized reduced chemical mechanisms. We’ll see some results for this later.

## Slide 102: Bray-Moss-Libby Model (1977)
Unburnt
Burnt
“Burnt Fraction”
Notes: To proceed with the flame front approach we adopt the Bray-Moss-Libby description of the subgrid burnt fraction. Now, I work in terms of the burnt, not the unburnt fraction (sorry). But there is a reason for this too. And this time it’s historical.
Now, in this example, the cell is completely mixed. The burnt fraction is the fraction of mass IN THE MIXED ZONE that is burnt. We assume that the burnt density can be computed and that the initial cell density can be computed and does not change.

## Slide 103: Rate of Reaction in the Mixed Reactor Zone
Unburnt
Burnt
Notes: Again, the develop the model we differentiate in time… For the case of Theta_0=0, note that the burnt and unburnt compositions are constant.

## Slide 104: Simple Case: Premixed and Unburnt
Ö. L. Gülder. Turbulent Premixed Flame Propagation Models for Different Combustion Regimes. In Proceedings of the Combustion Institute, volume 23, pages 743–750, 1990.
Notes: It remains that we find a model for the time rate of change of Theta. So what we do is to imagine a 1D turbulent flame front traversing the cell. Of course, the change in position of the front is the turbulent flame speed.
Now, there is a lot of good data on laminar flame speed or you can compute it using kinetics codes like PREMIX. On the other hand, the translation of S_L to S_T is where the trouble lies. Nevertheless, there are several models to choose from.
A caution, though, that Theirre Poinsot points out that the correlations used to determine the S_T formula often show differences that are not related only to u’. Other boundary factors may be important.

## Slide 105: Partially-Stirred Turbulent Batch Reactor
Fuel
Air
Premixed Reactants
Burnt Products
Turbulent Flame Speed
Turbulent Mixing
Notes: So, here is, to me, the most interesting slide. Let’s look at the batch reactor model for a partially premixed case. But, again, we will consider Theta_0=0, which I argue is consistent with the level of approximation made in EDC.
So, an interesting thing happens, which the math got right, but which took me some time to understand.
The form of the closure suggests, again, that we have a mixing term and a reaction term. However, when you work out the reaction term it cancels out the mixing term! Crazy! Is this right? What is going on?
Consider the sign of this term. If it is positive…
Note that it vanishes once Theta=1. But, up to that point, yes, the mean chemical source term only depends on the flame speed, not the mixing rate.
Is it possible for this term to be negative? Yes, as t increases zeta may be some finite value and theta increases depending on S_T. If tau_mix is small (fast mixing) the left term can dominate. This means the burnt fraction can go down. At some point, this leads to extinction.
To me what is interesting is that the balance of these terms has Damkohler number information. And I think this naturally leads to the framework for an extinction model.
To be clear, I am not saying I have a new extinction model formulated. But as Prof. Trouve has pointed out there is Critical Da=1 that should give extinction.

## Slide 106: The End